## Slide 1: Information Technology
Management Information Systems (MIS)
  Move large amounts of data
Decision Support Systems (DSS)
  Add decision making support
Expert System
  Recommend decision based on expert knowledge
Notes: <number>
<footer>
<header>
<date/time>

## Slide 2: Technology Selection

## Slide 3: Decision Support System
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: Decision Support System
Personnel
Accounting
Production
Marketing
Distribution
Other areas
Management
Information: reports, model results
Data
Computer system:
data processing
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5: Decision Support System
Management Information System
Personnel
Accounting
Production
Marketing
Distribution
Other areas
Management
Information: reports, model results
Data
Computer system:
data processing
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: Decision Support System
Decision Support System
Management Information System
What-if? analysis
Personnel
Accounting
Production
Marketing
Distribution
Other areas
Management
Information: reports, model results
Data
Decisions
Computer system:
data processing
Quantitative techniques
Figure 4.12
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: Artificial Intelligence
Neural networks
  Emulate interconnections in brain
Genetic algorithms
  Based on adaptive capabilities in nature
Fuzzy logic
  Simulate human ability to deal with ambiguity
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: Enterprise Software
Collect, analyze, and make decisions based on data
ERP - Enterprise Resource Planning
Managing wide range of processes
  Human resources, materials management, supply chains, accounting, finance, manufacturing, sales force automation, customer service, customer order entry
Finding hidden patterns through data mining

## Slide 9: Advanced Communications
Electronic data interchange (EDI)
Internet, extranets
Wireless communications
Teleconferencing & telecommuting
Bar coding, RFT
Virtual reality
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10: Manufacturing Technology
Numerically controlled (NC) machines
  Controlled by punched tape
Computer numerical controlled (CNC)
  Controlled by attached computer
Direct numerical control (DNC)
  Several NC machines controlled by single computer
Flexible manufacturing systems (FMS)
  Includes automated material handling
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11: Automated Material Handling
Conveyors
Automated guided vehicle (AGV)
Automated storage & retrieval system (ASRS)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: Flexible Manufacturing Systems (FMS)
Programmable machine tools
Controlled by common computer network
Combines flexibility with efficiency
Reduces setup & queue times
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: Flexible Manufacturing System
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: Flexible Manufacturing System
Parts
Finished
goods
Computer
control
room
Terminal
CNC Machine
CNC Machine
Pallet
Automatic tool changer
Figure 4.13
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15: Robotics
Programmable manipulators
Follow specified path
Better than humans with respect to
  Hostile environments
  Long hours
  Consistency
Adoption has been slowed by ineffective integration and adaptation of systems
Notes: <number>
<footer>
<header>
<date/time>

## Slide 16: e-Manufacturing
Real-time sharing of data with trading partners and customers to drive collaborative decisions
  CAD - uses software to create & modify designs
  GT- classifies designs to benefit from prior experience
  STEP - sets standards for communication
  CAPP - creates processing instructions for CAM
  CAM - uses programmable automation in manufacturing
Notes: <number>
<footer>
<header>
<date/time>

## Slide 17: Components of e-Manufacturing
Notes: <number>
<footer>
<header>
<date/time>

## Slide 18: Components of e-Manufacturing
Figure 4.14
eM
Products
Manufacture
Processes
Information
Technology
CAD
GT
CAE
CPC
PDM
Product life cycle
Product Definition
CNC machines
STEP
CAD/CAM
CAPP
Sourcing &
e-procurement
B2B, B2C
Bar codes, RFT, EDI
ERP
SCM, CRM
DSS/ES/AI
Internet, Intranet, extranet, satellites
FMS
Robotics
AGV, ASRS
Process control
Cells
and centers
Multiple factory sites & suppliers
Notes: <number>
<footer>
<header>
<date/time>

## Slide 19: Strategy to Operation
So far, we have looked at the ‘big picture’ of Process Selection Decisions
Equally important is the Operational Capabilities of the Processes

## Slide 20: Process Capability
Range of inherent variability in process
  Measured with control charts. WRONG!
Process cannot meet specifications if natural variability exceeds tolerances
3-sigma quality
  Specifications equal the process control limits WRONG!
6-sigma quality
  Specifications twice as large as control limits WRONG!
Notes: <number>
<footer>
<header>
<date/time>

## Slide 21: Process Capability
Range of inherent variability in process
  Measured with respect to design tolerances
3-sigma quality
  Process range equals the design tolerance limits
6-sigma quality
  Process range is twice as large as the design tolerance limits
Notes: <number>
<footer>
<header>
<date/time>

## Slide 22: Process Capability
(b) Design specifications and natural variation the same; process is capable of meeting specifications most the time.
Design Specifications
Process
(a) Natural variation exceeds design specifications; process is not capable of meeting specifications all the time.
Design Specifications
Process
Figure 15.5
Notes: <number>
<footer>
<header>
<date/time>

## Slide 23: Process Capability
Figure 15.5
(c) Design specifications greater than natural variation; process is capable of always conforming to specifications.
Design Specifications
Process
(d) Specifications greater than natural variation, but process off center; capable but some output will not meet upper specification.
Design Specifications
Process
Notes: <number>
<footer>
<header>
<date/time>

## Slide 24: Process Capability Measures
Process Capability Ratio
Cp =
=
tolerance range
process range
upper specification limit -
lower specification limit
6

## Slide 25: Computing Cp
Net weight specification = 9.0 oz  0.5 oz
Process mean = 8.80 oz
Process standard deviation = 0.12 oz
Cp =
= = 1.39
upper specification limit -
lower specification limit
6
9.5 - 8.5
6(0.12)
Example 15.6

## Slide 26: Six Sigma Program
First initiated at Motorola
Aims to reduce to the defect rates so that process range totally covers tolerance range – 3.4 defect per million
C_p > 2

## Slide 27: Process Capability Measures
Process Capability Index
Cpk = minimum
x - lower specification limit
3
=
upper specification limit - x
3
=
,

## Slide 28: Computing Cpk
Net weight specification = 9.0 oz  0.5 oz
Process mean = 8.80 oz
Process standard deviation = 0.12 oz
Cpk = minimum
= minimum , = 0.83
x - lower specification limit
3
=
upper specification limit - x
3
=
,
8.80 - 8.50
3(0.12)
9.50 - 8.80
3(0.12)
Example 15.7

## Slide 29: Pitfalls
Process may not be centered
Process may not be stable
Process output distribution may not be not Normal

## Slide 30: How to Select?
Process capability measures only indicate the desirability of a process in terms of its output variability with respect to design tolerances
Eventual selection of a process requires a QUANTIFICATION of cost arising from deviations from design due to process (in)capabilities!

## Slide 31
For quantification, we may use:
TAGUCHI LOSS FUNCTION
The Taguchi Loss Function relates poor conformance quality costs to process selection/improvement efforts

## Slide 32: Taguchi Loss Function
A loss function that penalizes deviations from the design target values symmetrically in a quadratic fashion.

## Slide 33: Example

## Slide 34
The Ops Manager of a small company is concerned about
the variability of the process.
Currently
the process mean is 0.30 cm and the standard deviation
is 0.075 cm.
The target value of the design is set at 0.30 cm and the design
specifications are such that the process has a capability
ratio of 0.95.

## Slide 35
The competition is very though in this industry and the customers of the company are now pushing for the implementation of a six-sigma program as in Motorola.
How much should the company be willing to invest in variability improvements if:
The expected loss for any unit produced at the tolerance limits (design specs) is estimated at $3.50 ; and the annual production is 100,000 units?

## Slide 36: Caution!
Taguchi Loss Function assumes a symmetric penalty behavior – may not be appropriate in some cases
Difficult to assess cost parameters
Environment may not be stable

## Slide 37: Dynamics of Process Selection
Product lifecycle
  + Product/Process Matrix
Product Profiling – identifies Market/Manufacturing Misalignment
Rumack Pharmaceuticals Example