## Slide 1: Chapter 17
Human Resources in Operations Management
To Accompany Russell and Taylor, Operations Management, 4th Edition,  2003 Prentice-Hall, Inc. All rights reserved.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 2: Human Resources in Strategic Planning
TQM recognizes importance of employees
Education & training viewed as long-term investments
Employees
  Have broad latitude in jobs
  Are trained in wide range of skills
  Are empowered to improve quality & service
Notes: <number>
<footer>
<header>
<date/time>

## Slide 3: Changes in HR Management
Skilled craftspeople
Scientific management
Assembly lines
Limitations of scientific management
Behavioral influences in job design
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: Behavioral Influences in Job Design
1. Horizontal job enlargement
2. Vertical job enlargement
3. Responsibility for job reliability and quality
4. Job rotation
5. Communications between workers
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5: Evolution of Job Design
1900s to 1960s
Task specialization
Minimal worker skills
Repetition
Minimal job training
Mass production
Piece-rate wages
Time as efficiency
Minimal job responsibility
Tight supervisory control
Scientific management/ assembly lines
1970s to 2000s
Horizontal job enlargement
Vertical job enlargement
Extensive job training
Job responsibility and empowerment
Job control
Training and education
Job rotation
Higher skill levels
Team problem solving
Worker interaction
Employee involvement
Focus on quality
Current trends
Figure 17.1
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: Elements of Job Design
TASK ANALYSIS
Description of tasks to be performed
Task sequence
Function of tasks
Frequency of tasks
Criticality of tasks
Relationship with other jobs/tasks
Performance requirements
Information requirements
Control requirements
Error possibilities
Tasks duration(s)
Equipment requirements
Table 17.1
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: Elements of Job Design
TASK ANALYSIS |  | 
Description of tasks to be performed Task sequence Function of tasks Frequency of tasks Criticality of tasks Relationship with other jobs/tasks Performance requirements Information requirements Control requirements Error possibilities Tasks duration(s) Equipment requirements |  | 
Table 17.1
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: Elements of Job Design
TASK ANALYSIS | WORKER ANALYSIS | 
Description of tasks to be performed Task sequence Function of tasks Frequency of tasks Criticality of tasks Relationship with other jobs/tasks Performance requirements Information requirements Control requirements Error possibilities Tasks duration(s) Equipment requirements | Capability requirements Performance requirements Evaluation Skill level Job training Physical requirements Mental stress Boredom Motivation Number of workers Level of responsibility Monitoring level Quality responsibility Empowerment level | 
WORKER ANALYSIS
Capability requirements
Performance requirements
Evaluation
Skill level
Job training
Physical requirements
Mental stress
Boredom
Motivation
Number of workers
Level of responsibility
Monitoring level
Quality responsibility
Empowerment level
Table 17.1
Notes: <number>
<footer>
<header>
<date/time>

## Slide 9: Elements of Job Design
TASK ANALYSIS | WORKER ANALYSIS | 
Description of tasks to be performed Task sequence Function of tasks Frequency of tasks Criticality of tasks Relationship with other jobs/tasks Performance requirements Information requirements Control requirements Error possibilities Tasks duration(s) Equipment requirements | Capability requirements Performance requirements Evaluation Skill level Job training Physical requirements Mental stress Boredom Motivation Number of workers Level of responsibility Monitoring level Quality responsibility Empowerment level | 
Table 17.1
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10: Elements of Job Design
TASK ANALYSIS | WORKER ANALYSIS | 
Description of tasks to be performed Task sequence Function of tasks Frequency of tasks Criticality of tasks Relationship with other jobs/tasks Performance requirements Information requirements Control requirements Error possibilities Tasks duration(s) Equipment requirements | Capability requirements Performance requirements Evaluation Skill level Job training Physical requirements Mental stress Boredom Motivation Number of workers Level of responsibility Monitoring level Quality responsibility Empowerment level | 
ENVIRONMENTAL ANALYSIS
Work place location
Process location
Temperature and humidity
Lighting
Ventilation
Safety
Logistics
Space requirements
Noise
Vibration
Table 17.1
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11: Elements of Job Design
TASK ANALYSIS | WORKER ANALYSIS | ENVIRONEMENTAL ANALYSIS
Description of tasks to be performed Task sequence Function of tasks Frequency of tasks Criticality of tasks Relationship with other jobs/tasks Performance requirements Information requirements Control requirements Error possibilities Tasks duration(s) Equipment requirements | Capability requirements Performance requirements Evaluation Skill level Job training Physical requirements Mental stress Boredom Motivation Number of workers Level of responsibility Monitoring level Quality responsibility Empowerment level | Work place location Process location Temperature and humidity Lighting Ventilation Safety Logistics Space requirements Noise Vibration
Table 17.1
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: Job Analysis
Study how job should be done
Tools:
  Process flowchart - analyze process steps
  Worker-machine chart - study time utilization
  Motion study - study human motions in tasks
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: Process Flowchart Symbols
Operation: An activity directly contributing to the product or service.
Storage: Store of the product or service.
Inspection: Examining the product or service for completeness, irregularities, or quality.
Transportation: Moving the product or service from one location to another.
Delay: The process having to wait.
Figure 17.2
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: Process Flowchart
Date: 9/11
Analyst: Calvin
Job: Copying Job
Page:
Desk operator fills out work order
Work order placed in “waiting job” box
Job picked up by operator and read
Job carried to appropriate copy machine
Operator waits for machine to vacate
Operator loads paper
Operator sets machine
Operator performs and completes job
Job filed alphabetically in completed shelves
Job waits for pick up
Job moved by cashier for pick up
Cashier completes transaction
Operator inspects job for irregularities
Cashier packages job (bag, wrap, or box)
Process Description
Process Symbols
Figure 17.3

## Slide 15: Process Flowchart
Date: 9/11
Analyst: Calvin
Job: Copying Job
Page:
Desk operator fills out work order
Work order placed in “waiting job” box
Job picked up by operator and read
Job carried to appropriate copy machine
Operator waits for machine to vacate
Operator loads paper
Operator sets machine
Operator performs and completes job
Job filed alphabetically in completed shelves
Job waits for pick up
Job moved by cashier for pick up
Cashier completes transaction
Operator inspects job for irregularities
Cashier packages job (bag, wrap, or box)
Process Description
Process Symbols
Figure 17.3

## Slide 16: Worker-Machine Chart
– 1
– 2
– 3
– 4
– 5
– 6
– 7
– 8
– 9
– 10
Key in customer data on card
Feed data card in
Position customer for photo
Take picture
Inspect card & trim edges
Idle
Idle
Idle
Idle
Photo/card processed
Accept card
Begin photo process
2.6
0.4
1.0
0.6
3.4
1.2
Job Photo-Id Cards Date 10/14
Time Time
(min) Operator (min) Photo Machine
Figure 17.4

## Slide 17: Worker-Machine Chart
– 1
– 2
– 3
– 4
– 5
– 6
– 7
– 8
– 9
– 10
Key in customer data on card
Feed data card in
Position customer for photo
Take picture
Inspect card & trim edges
Idle
Idle
Idle
Idle
Photo/card processed
Accept card
Begin photo process
2.6
0.4
1.0
0.6
3.4
1.2
Job Photo-Id Cards Date 10/14
Time Time
(min) Operator (min) Photo Machine
Figure 17.4
Summary
Operator Time % Photo Machine Time %
Work 5.8 63 4.8 52
Idle 3.4 37 4.4 48
Total 9.2 min 100% 9.2 Min 100%

## Slide 18: Motion Study
Frank & Lillian Gilbreth
Find one “best way” to do task
Divide task into therbligs
  Search, select, grasp, hold
Use videotape to study motions
Notes: <number>
<footer>
<header>
<date/time>

## Slide 19: General Guidelines For Motion Study
Efficient Use Of Human Body
  Work - simplified, rhythmic & symmetric
  Hand/arm motions - coordinated and simultaneous
  Employ full extent of physical capabilities
  Conserve energy - use machines, minimize distances, use momentum
  Tasks - simple, minimal eye contact & muscular effort, no unnecessary motions, delays or idleness
Notes: <number>
<footer>
<header>
<date/time>

## Slide 20: General Guidelines For Motion Study
Efficient Arrangement Of Workplace
  Tools, material, equipment - designated, easily accessible location
  Seating & work area - comfortable and healthy
Efficient Use Of Equipment
  Equipment & mechanized tools enhance worker abilities
  Use foot-operated equipment to relieve hand/arm stress
  Construct & arrange equipment to fit worker use
Notes: <number>
<footer>
<header>
<date/time>

## Slide 21: Work Measurement
Estimate standard time required to perform a task
Methods of performing work measurement
  Stopwatch time study
  Elemental standard time files
  Predetermined motion times
  Work sampling
Notes: <number>
<footer>
<header>
<date/time>

## Slide 22: Stopwatch Time Study Basic Steps
1. Establish the standard job method
5. Compute the average time (t )
4. Rate the worker’s performance (RF)
3. Study the job
2. Break down the job into elements
Notes: <number>
<footer>
<header>
<date/time>

## Slide 23: Stopwatch Time Study Basic Steps
ST = (NT)(1 + AF)
Standard Time = (normal cycle time) x (1 + allowance factor)
7. Compute the standard time
6. Compute the normal time
Normal Cycle Time = NT = Nt
Normal Time = (Elemental average) x (rating factor)
Nt = (t )(RF)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 24: Performing a Time Study
Time Study Observation Sheet
Identification of operation
Sandwich Assembly
Date 5/17
Operator
Approval
Observer
Smith
Jones
Russell
Cycles
Summary
1
2
3
4
5
6
7
8
9
10
t
Nt
RF
t
Place ham, cheese,
and lettuce on bread
1
2
3
4
Grasp and lay out bread slices
Spread mayonnaise
on both slices
Place top on sandwich,
Slice, and stack
t
t
t
t
R
R
R
R
.11
.44
.79
1.13
1.47
1.83
2.21
2.60
2.98
3.37
.04
.05
.05
.04
.06
.05
.06
.06
.07
.05
.53
.053
1.05
.056
.04
.38
.72
1.05
1.40
1.76
2.13
2.50
2.89
3.29
.07
.06
.07
.08
.08
.08
.07
.07
.10
.09
.77
.077
.077
1.00
.11
.12
.14
.12
.12
.13
.13
.13
.14
.14
1.28
1.28
1.10
.141
.93
.23
.55
1.25
1.60
1.96
2.34
2.72
3.12
3.51
.12
.10
.08
.09
.12
.10
.11
.11
.10
.10
1.03
1.03
1.10
.113
.33
.67
1.01
1.34
1.71
2.07
2.44
2.82
3.24
3.61
Figure 17.5

## Slide 25: Performing a Time Study
Time Study Observation Sheet
Identification of operation
Sandwich Assembly
Date 5/17
Operator
Approval
Observer
Smith
Jones
Russell
Cycles
Summary
1
2
3
4
5
6
7
8
9
10
t
Nt
RF
t
Place ham, cheese,
and lettuce on bread
1
2
3
4
Grasp and lay out bread slices
Spread mayonnaise
on both slices
Place top on sandwich,
Slice, and stack
t
t
t
t
R
R
R
R
.11
.44
.79
1.13
1.47
1.83
2.21
2.60
2.98
3.37
.04
.05
.05
.04
.06
.05
.06
.06
.07
.05
.53
.053
1.05
.056
.04
.38
.72
1.05
1.40
1.76
2.13
2.50
2.89
3.29
.07
.06
.07
.08
.08
.08
.07
.07
.10
.09
.77
.077
.077
1.00
.11
.12
.14
.12
.12
.13
.13
.13
.14
.14
1.28
1.28
1.10
.141
.93
.23
.55
1.25
1.60
1.96
2.34
2.72
3.12
3.51
.12
.10
.08
.09
.12
.10
.11
.11
.10
.10
1.03
1.03
1.10
.113
.33
.67
1.01
1.34
1.71
2.07
2.44
2.82
3.24
3.61
Example 17.3
Normal time = (Elemental average)(rating factor)
Nt = ( t )(RF) = (0.053)(1.05) = 0.056
Normal Cycle Time = NT = Nt = 0.387
ST = (NT) (1 + AF) = (0.387)(1+0.15) = 0.445 min
Average element time = t = = = 0.053
t
10
0.53
10

## Slide 26: Performing a Time Study
Time Study Observation Sheet
Identification of operation
Sandwich Assembly
Date 5/17
Operator
Approval
Observer
Smith
Jones
Russell
Cycles
Summary
1
2
3
4
5
6
7
8
9
10
t
Nt
RF
t
Place ham, cheese,
and lettuce on bread
1
2
3
4
Grasp and lay out bread slices
Spread mayonnaise
on both slices
Place top on sandwich,
Slice, and stack
t
t
t
t
R
R
R
R
.11
.44
.79
1.13
1.47
1.83
2.21
2.60
2.98
3.37
.04
.05
.05
.04
.06
.05
.06
.06
.07
.05
.53
.053
1.05
.056
.04
.38
.72
1.05
1.40
1.76
2.13
2.50
2.89
3.29
.07
.06
.07
.08
.08
.08
.07
.07
.10
.09
.77
.077
.077
1.00
.11
.12
.14
.12
.12
.13
.13
.13
.14
.14
1.28
1.28
1.10
.141
.93
.23
.55
1.25
1.60
1.96
2.34
2.72
3.12
3.51
.12
.10
.08
.09
.12
.10
.11
.11
.10
.10
1.03
1.03
1.10
.113
.33
.67
1.01
1.34
1.71
2.07
2.44
2.82
3.24
3.61
Example 17.3
Normal time = (Elemental average)(rating factor)
Nt = ( t )(RF) = (0.053)(1.05) = 0.056
Normal Cycle Time = NT = Nt = 0.387
ST = (NT) (1 + AF) = (0.387)(1+0.15) = 0.445 min
Average element time = t = = = 0.053
t
10
0.53
10
How many sandwiches can be made in 2 hours?
= 269.7 or 270 sandwiches
120 min
0.445 min/sandwich

## Slide 27: Elemental Times
Predetermined Motion Times
Used for micromotions
Divide tasks into micromotions
  Grasp, reach, move, etc.
Time Measurement Units (TMU)
  0.0006 minutes, 100,000 per hour
Notes: <number>
<footer>
<header>
<date/time>

## Slide 28: MTM Table for MOVE
3/4 or less 2.0 2.0 2.0
1 2.5 2.9 3.4 2.3 2.5 1.00 0
2 3.6 4.6 5.2 2.9
4.9 5.7 6.7 3.6 7.5 1.06 2.2
4 6.1 6.9 8.0 4.3
…
20 19.2 18.2 22.1 15.6 37.5 1.39 12.5
A. Move object to other hand or against stop
B. Move object to approximate or indefinite location
C. Move object to exact location
TIME (TMU) WEIGHT ALLOWANCE
DISTANCE Hand in Weight Static
MOVED motion (lb) Dynamic constant
(INCHES) A B C B up to: factor TMU
Notes: <number>
<footer>
<header>
<date/time>

## Slide 29: Work Sampling - Basic Steps
Define the job activities
Determine number of observations
sample size is chosen on basis of
desired accuracy level –
statistical sampling
Notes: <number>
<footer>
<header>
<date/time>

## Slide 30: Work Sampling - Basic Steps
Determine length of sampling period
Conduct work sampling study, record observations
Periodically recompute number of observations
Notes: <number>
<footer>
<header>
<date/time>

## Slide 31: Learning Curves
Processing time decreases with worker learning (experience)
Time per unit decreases by constant percentage each time output doubles
Use to plan labor, budget & scheduling requirements
Notes: <number>
<footer>
<header>
<date/time>

## Slide 32: Learning Curves
Units produced
Processing time per unit
Figure 17.6
Notes: <number>
<footer>
<header>
<date/time>

## Slide 33: Learning Curves
tn = t1nb
Time required for the nth unit =
where
tn = time required for nth unit produced
t1 = time required for first unit produced
n = cumulative number of units produced
b = ln r/ln 2, where r is the learning curve percentage (decimal coefficient)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 34: Learning Curve Effect
Contract to produce 36 computers.
t1 = 18 hours, learning rate = 80%
What is time for 9th, 18th, 36th units?
t9 = (18)(9)ln(0.8)/ln 2 = (18)(9)-0.322
= (18)/(9)0.322 = (18)(0.493) = 8.874hrs
t18 = (18)(18)ln(0.8)/ln 2 = (18)(0.394) = 7.092hrs
t36 = (18)(36)ln(0.8)/ln 2 = (18)(0.315) = 5.674hrs
Example 17.7
Notes: <number>
<footer>
<header>
<date/time>

## Slide 35: Learning Curve for Mass Production Job
Standard time
End of improvement
Units produced
Processing time per unit
Figure 17.7
Notes: <number>
<footer>
<header>
<date/time>

## Slide 36: More on Learning Curves
Not effective for mass production jobs
Product modifications negate effects
Improvement can derive from sources besides learning
Industry-derived learning curve rates may be inappropriate
Notes: <number>
<footer>
<header>
<date/time>