## Slide 1: Supplement S5
Facility Location Models
Notes: <number>
<footer>
<header>
<date/time>

## Slide 2: Types Of Facilities
Heavy manufacturing
  Auto plants, steel mills, chemical plants
Light industry
  Small components mfg, assembly
Warehouse & distribution centers
Retail & service
Notes: <number>
<footer>
<header>
<date/time>

## Slide 3: Factors in Heavy Manufacturing Location
Construction costs
Land costs
Raw material and finished goods shipment modes
Proximity to raw materials
Utilities
Labor availability
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: Factors in Light Industry Location
Construction costs
Land costs
Easily accessible geographic region
Education & training capabilities
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5: Factors in Warehouse Location
Transportation costs
Proximity to markets
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: Factors in Retail Location
Proximity to customers
Location is everything
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: Global Location Factors
Government stability
Government regulations
Political and economic systems
Economic stability and growth
Exchange rates
Culture
Climate
Export import regulations, duties and tariffs
Raw material availability
Number and proximity of suppliers
Transportation and distribution system
Labor cost and education
Available technology
Commercial travel
Technical expertise
Cross-border trade regulations
Group trade agreements
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: Regional Location Factors
Labor (availability, education, cost and unions)
Proximity of customers
Number of customers
Construction/leasing costs
Land costs
Modes and quality of transportation
Transportation costs
Incentive packages
Governmental regulations
Environmental regulations
Raw material availability
Commercial travel
Climate
Infrastructure
Quality of life
Notes: <number>
<footer>
<header>
<date/time>

## Slide 9: Regional Location Factors
Community government
Local business regulations
Government services
Business climate
Community services
Taxes
Availability of sites
Financial Services
Community inducements
Proximity of suppliers
Education system
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10: Site Location Factors
Customer base
Construction/ leasing cost
Land cost
Site size
Transportation
Utilities
Zoning restrictions
Traffic
Safety/security
Competition
Area business climate
Income level
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11: Location Incentives
Tax credits
Relaxed government regulation
Job training
Infrastructure improvement
Money
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: Location Analysis Techniques
Location rating factor
Center-of-gravity
Load-distance
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: Location Rating Factor
Identify important factors
Weight factors (0.00 - 1.00)
Subjectively score each factor (0 - 100)
Sum weighted scores
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: Location Factor Rating
Labor pool and climate
Proximity to suppliers
Wage rates
Community environment
Proximity to customers
Shipping modes
Air service
LOCATION FACTOR
.30
.20
.15
.15
.10
.05
.05
WEIGHT
80
100
60
75
65
85
50
Site 1
65
91
95
80
90
92
65
Site 2
90
75
72
80
95
65
90
Site 3
SCORES (0 TO 100)
Weighted Score Site 1 = (0.30)(80) = 24
Example S5.1
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15: Location Factor Rating
Labor pool and climate
Proximity to suppliers
Wage rates
Community environment
Proximity to customers
Shipping modes
Air service
LOCATION FACTOR
.30
.20
.15
.15
.10
.05
.05
WEIGHT
80
100
60
75
65
85
50
Site 1
65
91
95
80
90
92
65
Site 2
90
75
72
80
95
65
90
Site 3
SCORES (0 TO 100)
24.00
20.00
9.00
11.25
6.50
4.25
2.50
77.50
Site 1
19.50
18.20
14.25
12.00
9.00
4.60
3.25
80.80
Site 2
27.00
15.00
10.80
12.00
9.50
3.25
4.50
82.05
Site 3
WEIGHTED SCORES
Example S5.1
Weighted Score Site 1 = (0.30)(80) = 24
Notes: <number>
<footer>
<header>
<date/time>

## Slide 16: Center-of-Gravity Technique
Locate facility at center of geographic area
Based on weight and distance traveled
Establish grid-map of area
Identify coordinates and weights shipped for each location
Notes: <number>
<footer>
<header>
<date/time>

## Slide 17: Grid-Map Coordinates
where,
x, y = coordinates of the new facility at center of gravity
xi, yi = coordinates of existing facility i
Wi = annual weight shipped from facility i

n
Wi
i = 1

xiWi
i = 1
n
x =

n
Wi
i = 1

yiWi
i = 1
n
y =
x1
x2
x3
x
y2
y
y1
y3
1 (x1, y1), W1
2 (x2, y2), W2
3 (x3, y3), W3
Figure S5.1
Notes: <number>
<footer>
<header>
<date/time>

## Slide 18: Center-of-Gravity Technique
A B C D
x 200 100 250 500
y 200 500 600 300
Wt 75 105 135 60
Example S5.2
y
700
500
600
400
300
200
100
0
x
700
500
600
400
300
200
100
A
B
C
D
(135)
(105)
(75)
(60)
Miles
Miles
Notes: <number>
<footer>
<header>
<date/time>

## Slide 19: Center-of-Gravity Technique
y
700
500
600
400
300
200
100
0
x
700
500
600
400
300
200
100
A
B
C
D
(135)
(105)
(75)
(60)
Miles
Miles
A B C D
x 200 100 250 500
y 200 500 600 300
Wt 75 105 135 60
Example S5.2
x = = = 238
n

Wi
i = 1

xiWi
i = 1
n

n
Wi
i = 1

yiWi
i = 1
n
y = = = 444
(200)(75) + (500)(105) + (600)(135) + (300)(60)
75 + 105 + 135 + 60
(200)(75) + (100)(105) + (250)(135) + (500)(60)
75 + 105 + 135 + 60
Notes: <number>
<footer>
<header>
<date/time>

## Slide 20: Center-of-Gravity Technique
A B C D
x 200 100 250 500
y 200 500 600 300
Wt 75 105 135 60
Example S5.2
y
700
500
600
400
300
200
100
0
x
700
500
600
400
300
200
100
A
B
C
D
(135)
(105)
(75)
(60)
Miles
Miles
Center of gravity (238, 444)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 21: Load-Distance Technique
Compute Load x Distance for each site
Choose site with lowest Load x Distance
Distance can be actual or straight-line
Notes: <number>
<footer>
<header>
<date/time>

## Slide 22: Load-Distance Calculations

li di
i = 1
n
LD =
LD = the load-distance value
li = the load expressed as a weight, number of trips or units
being shipped from the proposed site and location i
di = the distance between the proposed site and location i
di = (xi - x)2 + (yi - y)2
(x,y) = coordinates of proposed site
(xi , yi) = coordinates of existing facility
where,
where,
Notes: <number>
<footer>
<header>
<date/time>

## Slide 23: Load-Distance Example
Potential Sites
Site X Y
1 360 180
2 420 450
3 250 400
Suppliers
A B C D
X 200 100 250 500
Y 200 500 600 300
Wt 75 105 135 60
Compute distance from each site to each supplier
= (200-360)2 + (200-180)2
dA = (xA - x1)2 + (yA - y1)2
Site 1
= 161.2
= (100-360)2 + (500-180)2
dB = (xB - x1)2 + (yB - y1)2
= 412.3
dC = 434.2
dD = 184.4
Example S5.3
Notes: <number>
<footer>
<header>
<date/time>

## Slide 24: Load-Distance Example
Site 2
dA = 333
dC = 226.7
dB = 323.9
dD = 170
Site 3
dA = 206.2
dC = 200
dB = 180.4
dD = 269.3
Compute load-distance
i = 1
n

li di
LD =
Site 1 = (75)(161.2) + (105)(412.3) + (135)(434.2) + (60)(434.4) = 125,063
Site 2 = (75)(333) + (105)(323.9) + (135)(226.7) + (60)(170) = 99,789
Site 3 = (75)(206.2) + (105)(180.3) + (135)(200) + (60)(269.3) = 77,555*
* Choose site 3
Example S5.3
Notes: <number>
<footer>
<header>
<date/time>

## Slide 25: Location Analysis
Exhibit S5.1

## Slide 26: Location Analysis
Exhibit S5.2

## Slide 27: Location Analysis
Exhibit S5.3

## Slide 28: Location Analysis
Exhibit S5.4