## Slide 1: The Design Process
Ch 5 - 7
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
No
Idea
generation
Final
design
Preliminary
design
Feasibility
study
Process
planning
Product
feasible?
Yes
Prototype
Manufacturing
Design & Manufacturing
Specifications

## Slide 2: 1. Idea Generation
Provides basis for entry into market
Sources of ideas
Follows from marketing strategy
  Identifies, defines, & selects best market opportunities
Notes: One notion which might be discussed at this stage is the attempts by manufacturers to add information to an existing good rather than develop a new good.

## Slide 3: Idea Generation Sources
Ch 5 - 8
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
Suppliers, distributors, salespersons
Trade journals and other published material
Warranty claims, customer complaints, failures
Customer surveys, focus groups, interviews
Field testing, trial users
Research and development
Market need (60-80%); engineering & operations (20%); technology; competitors; inventions; employees

## Slide 4: More Idea Generators
Ch 5 - 9
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
Perceptual Maps
  visual comparison of customer perceptions
Benchmarking
  comparing product/service against best-in-class
Reverse engineering
  dismantling competitor’s product to improve your own product

## Slide 5: Perceptual Map Of Breakfast Cereals
Ch 5 - 10
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
Good taste
Bad taste
High nutrition
Low nutrition
Cocoa Puffs
Rice
Krispies
Wheaties
Cheerios
Shredded
Wheat

## Slide 6: 2. Feasibility Study
Ch 5 - 11
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
Market Analysis
Economic Analysis
Technical / Strategic Analysis

## Slide 7: Customer Requirements Assessment – (QFD)
House of Quality
Customer Requirements
Product Characteristics
Identifies & positions key product benefits
  Stated in core benefits proposition (CBP)
  Example: Long lasting with more power (Sears’ Die Hard Battery)
Identifies detailed list of product attributes desired by customer
  Focus groups or 1-on-1 interviews

## Slide 8: Function Specification
House of Quality
Customer Requirements
Product Characteristics
Defines product in terms of how the product would meet desired attributes
Identifies product’s engineering characteristics
  Example: printer noise (dB)
Prioritizes engineering characteristics
May rate product compared
to competitors’

## Slide 9: Product Specification
Determines how product will be made
Gives product’s physical specifications
  Example: Dimensions, material etc.
Defined by engineering drawing
Done often on computer
  Computer-Aided
  Design (CAD)
House of Quality
Product
Characteristics
Component Specifications

## Slide 10
Broad categories of evaluation criteria for assessing design options
FEASIBILITY
How difficult is it?
ACCEPTABILITY
How worthwhile is it?
VULNERABILITY
What could go wrong?
THE CRITERIA FOR ASSESSING PROPOSED DESIGN OPTIONS
What INVESTMENT both managerial and financial will be needed?
What RETURN
in terms of financial and performance improvement will it give?
What RISKS
do we run if things go wrong?

## Slide 11: 3. Preliminary Design
Ch 5 - 12
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
Create form & functional design
Build prototype
Test prototype
Revise prototype
Retest

## Slide 12: 4. Form Design (How The Product Looks)
Ch 5 - 13
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
© 1984-1994 T/Maker Co.

## Slide 13: 5. Functional Design (How The Product Performs)
Ch 5 - 14
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
Reliability
  probability product performs intended function for specified length of time
Maintainability
  ease and/or cost or maintaining/repairing product

## Slide 14: 6. Final Design & Process Planning
Ch 5 - 16
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
Produce detailed drawings & specifications
Create workable instructions for manufacture
Select tooling & equipment
Prepare job descriptions
Determine operation & assembly order
Program automated machines

## Slide 15: Product Development Stages
Idea generation
Assessment of firm’s ability to carry out
Customer Requirements
Functional Specification
Product Specifications
Design Review
Test Market
Introduction to Market
Evaluation
Scope of product development team
Scope of design for manufacturability and value engineering teams

## Slide 16: How to Improve Design Process ?

## Slide 17: Lean Design Practices – Japanese Experience
Leadership
Teamwork
Communication
Simultaneous Development

## Slide 18: Improving The Design Process – General Principles
Ch 5 - 18
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
1. Design teams
2. Concurrent design
3. Design for ease
4. Design for robustness
5. Measure design process quality/performance
6. Utilize Quality Function Deployment

## Slide 19: Measures Of Design Performance
Ch 5 - 35
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
1. Number of component parts and product options
2. Percentage of standard parts
3. Use of existing manufacturing resources
4. Cost of first production run
5. First six months cost of engineering changes
6. First year cost of field service repair
7. Total product cost
8. Total product sales
9. Sustainable development

## Slide 20: Metrics for Design Quality
Percent of revenue from new products or services
Percent of products capturing 50% or more of the market
Percent of process initiatives yielding a 50% or more improvement in effectiveness
Percent of suppliers engaged in collaborative design
Notes: <number>
<footer>
<header>
<date/time>

## Slide 21: Metrics for Design Quality
Percent of parts that can be recycled
Percent of parts used in multiple products
Average number of components per product
Percent of parts with no engineering change orders
Things gone wrong
Notes: <number>
<footer>
<header>
<date/time>

## Slide 22
Product development performance measures in automobile industry?
(The Machine that Changed the World, Fig. 5.1)

## Slide 23: Improving The Design Process – General Principles
Ch 5 - 18
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
1. Design teams
2. Concurrent design
3. Design for ease
4. Design for robustness
5. Measure design process quality/performance
6. Utilize Quality Function Deployment

## Slide 24: Design Teams
Ch 5 - 19
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
Marketing, manufacturing, engineering
Suppliers, dealers, customers
Lawyers, accountants, insurance companies

## Slide 25: Concurrent Design
Ch 5 - 20
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
Customers
Marketing
Design
Engineering
Suppliers
Production

## Slide 26: Concurrent Design
Ch 5 - 21
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
Also, simultaneous or concurrent engineering
Simultaneous decision making by design teams
Integrates product design & process planning
Details of design more decentralized
Encourages price-minus not cost-plus pricing
Needs careful scheduling - tasks done in parallel

## Slide 27: General Performance Specifications
Ch 5 - 22
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
Instructions to supplier:
  “Design a set of brakes that can stop a 2200 pound car from 60 miles per hour in 200 feet ten times in succession without fading. The brakes should fit into a space 6” x 8” x 10” at the end of each axle and be delivered to the assembly plant for $40 a set.”
Supplier submits design specifications and prepares a prototype for testing.

## Slide 28: NEW Role Of Design Engineer
Ch 5 - 23
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
No longer totally responsible for product design
Responsible for more than what was traditionally considered “design”
Merging of design engineer and manufacturing engineer

## Slide 29: Design for __________
Design for Manufacture (DFM)
Design for Assembly (DFA)
Design for Maintenance/Repair
Design for Environment
Design for Ease in ___________

## Slide 30: Design For Manufacture
Ch 5 - 24
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
Design a product for easy & economical production
Consider manufacturability early in the design phase
Identify easy-to-manufacture product-design characteristics
Use easy to fabricate & assemble components
Integrate product design with process planning

## Slide 31: DFM Guidelines
Ch 5 - 25
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
1. Minimize the number of parts
2. Develop a modular design
3. Design parts for multi-use
4. Avoid separate fasteners
5. Eliminate adjustments
6. Design for top-down assembly

## Slide 32
Ch 5 - 26
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
7. Design for minimum handling
8. Avoid tools
9. Minimize subassemblies
10. Use standard parts when possible
11. Simplify operations
12. Design for efficient and adequate testing
13. Use repeatable & understood processes
14. Analyze failures
15. Rigorously assess value

## Slide 33: Design Simplification Example
Ch 5 - 27
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
(a) The original design
(b) Revised design
(c) Final design
Design for push-and-snap
assembly
One-piece base &
elimination of fasteners
Assembly using
common fasteners

## Slide 34: More Ways for Design Improvements
Ch 5 - 28
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
Standardization
  uses commonly available parts
  reduces costs & inventory
Modular design
  combines standardized building blocks/modules into unique products
  products designed in easily segmented components
  adds flexibility to production & marketing

## Slide 35: Design For Assembly (DFA)
Ch 5 - 29
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
Procedure for reducing number of parts
Evaluate methods for assembly
Determine assembly sequence

## Slide 36: Analyzing Failures
Ch 5 - 30
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
Failure Mode and Effects Analysis (FMEA)
  a systematic approach for analyzing causes & effects of failures
  prioritizes failures
  attempts to eliminate causes
Fault Tree Analysis (FTA)
  study interrelationship between failures

## Slide 37: Failure Mode & Effects Analysis
Ch 5 - 31
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e

## Slide 38: Fault Tree For Potato Chips
Ch 5 - 32
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
And
Or

## Slide 39: Design For Environment
Ch 5 - 34
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
Design from recycled material
Use materials which can be recycled
Design for ease of repair
Minimize packaging
Minimize material & energy used during manufacture, consumption & disposal

## Slide 40: Design For Robustness
Ch 5 - 42
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
Product can fail due to poor design quality
Products subjected to many conditions
Robust design studies
  controllable factors - under designer’s control
  uncontrollable factors - from user or environment
Designs products for consistent performance

## Slide 41: Consistency Is Important
Ch 5 - 43
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
Consistent errors are easier to correct than random errors
Parts within tolerances may yield assemblies which aren’t
Consumers prefer product characteristics near their ideal values

## Slide 42: Robust Design
Product is designed so that small variations in production or assembly do not adversely affect the product
Notes: After discussing the concept of robust design, you might identify a product and ask students to identify the use of robust design in its production. (One example is the use of the plastic seal on the inside of soda bottle caps)

## Slide 43: Value Analysis (Engineering)
Focuses on design improvement during production
Seeks improvements leading either to a better product or a product which can be more economically produced.
Notes: You might suggest that your students view value analysis as value engineering during, rather than prior to, production. Value analysis helps continually improve both design and production methodology.

## Slide 44: Value Analysis (Engineering)
Ch 5 - 33
© 1998 by Prentice-Hall Inc
Russell/Taylor Oper Mgt 2/e
Ratio of value / cost
Assessment of value :
  1. Can we do without it?
  2. Does it do more than is required?
  3. Does it cost more than it is worth?
  4. Can something else do a better job
  5. Can it be made by less costly method, tools, material?
  6. Can it be made cheaper, better or faster by someone else?

## Slide 45: Manufacturability and Value Engineering
Benefits:
  reduced complexity of products
  additional standardization of products
  improved functional aspects of product
  improved job design and job safety
  improved maintainability of the product
  robust design
Notes: Manufacturability and value engineering encompass many issues. You may wish to stress the point that we consider in detail not only what the product is, but how it is to be produced and maintained - the best design is optimized across all these activities, not just one or another.

## Slide 46: Cost Reduction via Value Eng’g

## Slide 47: Technology in Design
CAD - Computer Aided Design
  Assists in creating and modifying designs
CAE - Computer Aided Engineering
  Tests & analyzes designs on computer screen
CAD/CAM - Design & Manufacturing
  Automatically converts CAD data into processing instructions for computer controlled equipment
Notes: <number>
<footer>
<header>
<date/time>

## Slide 48: Benefits of CAD
Produces better designs faster
Builds database of designs and creates documentation to support them
Shortens time to market
Reduces time to manufacture
Enlarges design possibilities
Enhances communication and promotes innovation in design teams
Notes: <number>
<footer>
<header>
<date/time>

## Slide 49: Collaborative Product Commerce
Share and work on design files in real time from physically separate locations, typically over the internet
Accelerates product development
Helps resolve product launch issues
Improves the quality of design

## Slide 50: Customer Requirements Assessment – (QFD)
House of Quality
Customer Requirements
Product Characteristics
Identifies & positions key product benefits
  Stated in core benefits proposition (CBP)
  Example: Long lasting with more power (Sears’ Die Hard Battery)
Identifies detailed list of product attributes desired by customer
  Focus groups or 1-on-1 interviews

## Slide 51: Quality Function Deployment (QFD)
Translates the “voice of the customer” into technical design requirements
Displays requirements in matrix diagrams
First matrix called “house of quality”
Series of connected houses
Notes: <number>
<footer>
<header>
<date/time>

## Slide 52: House of Quality
Notes: <number>
<footer>
<header>
<date/time>

## Slide 53: House of Quality
Trade-off matrix
Design characteristics
Customer requirements
Target values
Relationship matrix
Competitive assessment
Importance
1
2
3
4
5
6
Figure 3.7
Notes: <number>
<footer>
<header>
<date/time>

## Slide 54: House of Quality
Figure 3.8
Irons well
Easy and safe to use
Competitive Assessment
Customer Requirements 1 2 3 4 5
Presses quickly 9 B A X
Removes wrinkles 8 AB X
Doesn’t stick to fabric 6 X BA
Provides enough steam 8 AB X
Doesn’t spot fabric 6 X AB
Doesn’t scorch fabric 9 A XB
Heats quickly 6 X B A
Automatic shut-off 3 ABX
Quick cool-down 3 X A B
Doesn’t break when dropped 5 AB X
Doesn’t burn when touched 5 AB X
Not too heavy 8 X A B
Notes: <number>
<footer>
<header>
<date/time>

## Slide 55: House of Quality
Figure 3.9
Energy needed to press
Weight of iron
Size of soleplate
Thickness of soleplate
Material used in soleplate
Number of holes
Size of holes
Flow of water from holes
Time required to reach 450º F
Time to go from 450º to 100º
Protective cover for soleplate
Automatic shutoff
Customer Requirements
Presses quickly - - + + + -
Removes wrinkles + + + + +
Doesn’t stick to fabric - + + + +
Provides enough steam + + + +
Doesn’t spot fabric + - - -
Doesn’t scorch fabric + + + - +
Heats quickly - - + -
Automatic shut-off +
Quick cool-down - - + +
Doesn’t break when dropped + + + +
Doesn’t burn when touched + + + +
Not too heavy + - - - + -
Irons well
Easy and safe to use
Notes: <number>
<footer>
<header>
<date/time>

## Slide 56: House of Quality
Figure 3.10
Energy needed to press
Weight of iron
Size of soleplate
Thickness of soleplate
Material used in soleplate
Number of holes
Size of holes
Flow of water from holes
Time required to reach 450º
Time to go from 450º to 100º
Protective cover for soleplate
Automatic shutoff
-
-
+
+
+
Notes: <number>
<footer>
<header>
<date/time>

## Slide 57: House of Quality
Figure 3.11
Energy needed to press
Weight of iron
Size of soleplate
Thickness of soleplate
Material used in soleplate
Number of holes
Size of holes
Flow of water from holes
Time required to reach 450º
Time to go from 450º to 100º
Protective cover for soleplate
Automatic shutoff
Units of measure ft-lb lb in. cm ty ea mm oz/s sec sec Y/N Y/N
Iron A 3 1.4 8x4 2 SS 27 15 0.5 45 500 N Y
Iron B 4 1.2 8x4 1 MG 27 15 0.3 35 350 N Y
Our Iron (X) 2 1.7 9x5 4 T 35 15 0.7 50 600 N Y
Estimated impact 3 4 4 4 5 4 3 2 5 5 3 0
Estimated cost 3 3 3 3 4 3 3 3 4 4 5 2
Targets 1.2 8x5 3 SS 30 30 500
Design changes * * * * * * *
Objective measures
Notes: <number>
<footer>
<header>
<date/time>

## Slide 58: House of Quality
Figure 3.12
Notes: <number>
<footer>
<header>
<date/time>

## Slide 59: Series of QFD Houses
Notes: <number>
<footer>
<header>
<date/time>

## Slide 60: Series of QFD Houses
Customer requirements
House of quality
Product characteristics
A-1
Product characteristics
Parts deployment
Part characteristics
A-2
Part characteristics
Process planning
Process characteristics
A-3
Process characteristics
Operating requirements
Operations
A-4
Figure 3.13
Notes: <number>
<footer>
<header>
<date/time>

## Slide 61: Benefits of QFD
Promotes better understanding of customer demands
Promotes better understanding of design interactions
Involves manufacturing in the design process
Breaks down barriers between functions and departments
Provides documentation of the design process
Notes: <number>
<footer>
<header>
<date/time>

## Slide 62: Characteristics of Services
Services are intangible
Service output is variable
Service have higher customer contact
Services are perishable
Service inseparable from delivery
Tend to be decentralized and dispersed
Consumed more often than products
Services can be easily emulated
Notes: <number>
<footer>
<header>
<date/time>

## Slide 63: A Well-Designed Service System is
FedEx
Consistent with firm’s strategic focus
User friendly
Robust
Easy to sustain
Effectively linked between front & back office
Cost effective
Visible to customer
Notes: <number>
<footer>
<header>
<date/time>

## Slide 64: The Service Design Process
Notes: <number>
<footer>
<header>
<date/time>

## Slide 65: The Service Design Process
Figure 3.14
Performance Specifications
Service
Delivery Specifications
Physical items
Sensual benefits
Psychological benefits
Design Specifications
Service Provider
Customer
Customer requirements
Customer expectations
Activities
Facility
Provider skills
Cost and time estimates
Schedule
Deliverables
Location
Service Concept
Service Package
Desired service experience
Targeted customer
Notes: <number>
<footer>
<header>
<date/time>

## Slide 66: Figure 3.15 Blueprint for an Installment Lending Operation
Loan application
Branch
Officer
Pay book
Line of visibility
Deny
1 day
2 days
3 days
Confirm
Fail point Customer wait Employee decision
F
F
F
F
F
F
W
30 min. – 1 hr.
Decline
Receive payment
Final payment
Notify customer
Close account
Confirm
Delinquent
Issue check
Print payment book
Accept
Verify income data
Initial screening
Employer
Bank accounts
Credit check
Credit bureau
Data base records
Branch records
Accounting
Verify payor
W
W

## Slide 67: Design for High-Contact Services
DESIGN DECISION HIGH-CONTACT SERVICE LOW-CONTACT SERVICE
Facility location | Convenient to customer | Near labor or transportation
Facility layout | Must look presentable, accommodate customer needs, and facilitate interaction with customer | Designed for efficiency
Quality control | More variable since customer is involved in process; customer expectations and perceptions of quality may differ; customer present when defects occur | Measured against established standards; testing and rework possible to correct defects
Capacity | Excess capacity required to handle peaks in demand | Planned for average demand
Table 3.2

## Slide 68: Design for High-Contact Services
DESIGN DECISION HIGH-CONTACT SERVICE LOW-CONTACT SERVICE
Worker skills | Must be able to interact well with customers and use judgment in decision making | Technical skills
Scheduling | Must accommodate customer schedule | Customer concerned only with completion date
Service process | Mostly front-room activities; service may change during delivery in response to customer | Mostly back-room activities; planned and executed with minimal interference
Service package | Varies with customer; includes environment as well as actual service | Fixed, less extensive
Table 3.2